## Slide 1
Information regarding twenty-two steel benchmark frames is provided. As a collection, the frames represent a variety of practical geometries with a wide range of sensitivities to second-order effects.
All of the frames are planar and the majority of them have been presented in the literature previously (references provided). All sections are oriented to bend about their major axis (with the exception of two frames), and the structures are all assumed to be fully braced out-of-plane.
The member sizes, material properties, support conditions, and loading ratios are the same as those in the original cited work. As such, the information provided for most frames is in US customary units.
Changes were made to the original load magnitudes (while retaining original load ratios) to assure that each benchmark structure supports sufficient load such that its strength is close to its design capacity. Details in this regard are available in an article by the authors1. All frames represent realistic designs that satisfy service-load criteria.
Finite element models have been provided on Mendeley Data for both perfect and imperfect geometries. Imperfect geometries include global sway of H/500 (with H = frame height) in the direction provided herein.
Description of Benchmark Frames
R.D. Ziemian & C.W. Ziemian; July 2021
1 C.W. Ziemian, R.D. Ziemian, Efficient geometric nonlinear elastic analysis for design of steel structures: Benchmark studies, Journal of Constructional Steel Research, 2021, in press.

## Slide 2
Brief overview of the frames and load cases

## Slide 3
30 ft
15 ft
Nominal Loads
Gravity (L/D = 2)
D = 79.202 kip
Lr = 158.405 kip
Wind
W = 69.70 kip
Initial imperfection
Global sway D0 = H/500 (rightward)
Material
E = 29,000 ksi
Fy = 36 ksi
W14x68
W18x35
W14x68
1.2D + 1.6Lr
0.5W
Frame 1: Single story portal frame
Load combination investigated
1.2D + 1.6Lr + 0.5W
1.2D + 1.6Lr
Reference
R.D. Ziemian, Advanced methods of inelastic analysis in the limit states design of steel structures, Cornell University, 1990.

## Slide 4
40 ft
25 ft
25 ft
38.5 ft
Frame 2: Single story gabled frame
W18x106
W18x106
W12x50
W12x50
1.2D + 0.5Lr
1.0W2
Reference
Schimizze, Comparison of P-Delta Analyses of Plane Frames using Commercial Structural Analysis Programs and Current AISC Design Specifications, Virginia Tech, 2001.
40 ft
1.0W1
Nominal Loads
Gravity (L/D = 2)
D = 0.374 kip/ft
Lr = 0.749 kip/ft
Wind
W1 = 5.627 kip
W2 = 6.046 kip
Initial imperfection
Global sway D0 = H/500 (rightward)
Material
E = 29,000 ksi
Fy = 36 ksi
Load combination investigated
1.2D + 0.5Lr + 1.0W

## Slide 5
12 ft
W8x31
Reference
G.G. Deierlein, J.F. Hajjar, J.A. Yura, D.W. White, W.F. Baker, Proposed new provisions for frame stability using second-order analysis, Proceedings - Annual Stability Conference, Structural Stability Research Council. (2002) 1–20.
8 ft
10 ft
W
G
W8x31
W8x18
W12x26
W8x31
W8x31
9 ft
W8x18
W12x26
Frame 3:
Nominal Loads
Gravity
G = 475.137 kip
Wind
W = 3.088 kip
Initial imperfection
Global sway D0 = H/500 (rightward)
Material
E = 29,000 ksi
Fy = 50 ksi
Load combination investigated
1.0G + 1.0W

## Slide 6
Frame 4
Rigid
35 ft
35 ft
35 ft
18 ft
W10x49
W10x49
Rigid
W27x84
W27x84
W27x84
1.2D + 1.6Lr
Single-story, 11-bay structure with ten leaning columns. This structure is representative of low-rise industrial buildings in which low wind exposure and heavy equipment suspended from the ceiling contribute to large second-order effects. Only two leaning columns are displayed (above) for simplicity.
Reference
A.E. Maleck, Second-order inelastic and modiﬁed elastic analysis and design evaluation of planar steel frames, Georgia Institute of Technology, 2001.
Nominal Loads
Gravity (L/D = 0.5)
Roof distributed
D = 3.209 kip/ft
Lr = 1.604 kip/ft
Roof concentrated
D = 449.21 kip
Lr = 224.60 kip
Initial imperfection
Global sway D0 = H/500 (rightward)
Material
E = 29,000 ksi
Fy = 50 ksi
Load combination investigated
1.2D + 1.6Lr
1.2D + 1.6Lr
1.2D + 1.6Lr

## Slide 7
Reference
J.M. Martinez-Garcia, R.D. Ziemian, Benchmark studies to compare frame stability provisions, Structural Stability Research Council - Proceedings 2006 Annual Stability Conference. (2006) 425–442.
Frame 5
24 ft
18 ft
12 ft
W8x40
8 ft
W18x50
W8x58
W8x40
W14x30
0.5 W2
1.2D + 1.6Lr
1.2D + 1.6Lr
Nominal Loads
Gravity (L/D = 1.5)
Roof: D = 1.824 kip/ft
Lr = 2.736 kip/ft
Wind
W1 = 4.672 kip
W2 = 7.084 kip
Initial imperfection
Global sway D0 = H/500 (leftward)
Material
E = 29,000 ksi
Fy = 50 ksi
Load combination investigated
1.2D + 1.6Lr +0.5W
0.5 W1
0.5 W1

## Slide 8
Reference
J.M. Martinez-Garcia, R.D. Ziemian, Benchmark studies to compare frame stability provisions, Structural Stability Research Council - Proceedings 2006 Annual Stability Conference. (2006) 425–442.
Frame 6
24 ft
18 ft
12 ft
W8x40
8 ft
W18x50
W8x58
W8x40
W14x30
0.5 W2
1.2D + 1.6Lr
1.2D + 1.6Lr
Nominal Loads
Gravity (L/D = 1.5)
Roof: D = 1.85 kip/ft
Lr = 2.78 kip/ft
Wind
W1 = 4.752 kip
W2 = 7.117 kip
0.5 W1
0.5 W1
Initial imperfection
Global sway D0 = H/500 (leftward)
Material
E = 29,000 ksi
Fy = 50 ksi
Load combination investigated
1.2D + 1.6Lr +0.5W

## Slide 9
Frame 7
24 ft
18 ft
W8x28
W18x71
W8x28
W6x9
W12x58
12 ft
8 ft
W4x13 (typ)
Only tension
brace modeled
Reference
J.M. Martinez-Garcia, R.D. Ziemian, Benchmark studies to compare frame stability provisions, Structural Stability Research Council - Proceedings 2006 Annual Stability Conference. (2006) 425–442.
Nominal Loads
Gravity (L/D = 1.5)
Roof: D = 0.841 kip/ft
Lr = 1.346 kip/ft
Wind
W1 = 13.158 kip
W2 = 19.739 kip
Initial imperfection
Global sway D0 = H/500 (leftward)
Material
E = 29,000 ksi
Fy = 50 ksi
Load combination investigated
1.2D + 1.6Lr +0.5W
0.5 W2
0.5 W1
0.5 W1
1.2D + 1.6Lr
1.2D + 1.6Lr

## Slide 10
Frame 8
NOTE re Member orientation
Beams: Major axis bending
Column: Minor axis bending
24 ft
18 ft
W10x60
W24x131
W10x60
W6x20
W16x100
12 ft
8 ft
W4x13 (typ)
Only tension
brace modeled
Reference
J.M. Martinez-Garcia, R.D. Ziemian, Benchmark studies to compare frame stability provisions, Structural Stability Research Council - Proceedings 2006 Annual Stability Conference. (2006) 425–442.
0.5 W2
0.5 W1
0.5 W1
1.2D + 1.6Lr
1.2D + 1.6Lr
Nominal Loads
Gravity (L/D = 1.5)
Roof: D = 1.924 kip/ft
Lr = 2.885 kip/ft
Wind
W1 = 14.78 kip
W2 = 22.16 kip
Initial imperfection
Global sway D0 = H/500 (leftward)
Material
E = 29,000 ksi
Fy = 50 ksi
Load combination investigated
1.2D + 1.6Lr +0.5W

## Slide 11
Reference
R.D. Ziemian, W. McGuire, G.G. Deierlein, Inelastic Limit States Design. Part I: Planar Frame Studies, Journal of Structural Engineering. 118 (1992). doi:10.1061/(asce) 0733-9445(1992)118:9(2532).
Frame 9
20 ft
48 ft
20 ft
15 ft
W8x15
W14x132
W14x120
W27x84
W36x170
W21x44
W27x102
W14x120
W14x109
1.2D + 0.5Lr
W8x13
Nominal Loads
Gravity (L/D = 1)
Roof: D = 2.785 kip/ft
Lr = 2.785 kip/ft
Floor: D = 3.623 kip/ft
L = 3.623 kip/ft
Initial imperfection
Global sway D0 = H/500 (leftward)
Material
E = 29,000 ksi
Fy = 36 ksi
Load combination investigated
1.2D + 1.6L + 0.5Lr
1.2D + 1.6L

## Slide 12
Reference
R.D. Ziemian; A. Miller, Inelastic analysis and design: frames with members in minor-axis bending, Journal of Structural Engineering. 123 (1997) 151.
Frame 10
20 ft
48 ft
W14x90
W14x90
W6x9
W8x40
W30x99
W14x90
W8x24
W36x160
W24x55
W30x99
NOTE re Member orientation
Beams: Major axis bending
Column: Minor axis bending
1.2D + 0.5Lr
1.2D + 1.6L
20 ft
15 ft
Nominal Loads
Gravity (L/D = 1)
Roof: D = 2.175 kip/ft
Lr = 2.175 kip/ft
Floor: D = 2.829 kip/ft
L = 2.829 kip/ft
Initial imperfection
Global sway D0 = H/500 (leftward)
Material
E = 29,000 ksi
Fy = 36 ksi
Load combination investigated
1.2D + 1.6L + 0.5Lr

## Slide 13
Frame 11
20’
20’
15’-0”
W12x87
W10x60
W10x60
W10x60
W10x77
W10x77
W10x68
W10x68
W12x87
W12x87
15’-0”
7’-6”
7’-6”
W10x39
W10x39
1.2D + 1.0L
W
Reference
Schimizze, Comparison of P-Delta Analyses of Plane Frames using Commercial Structural Analysis Programs and the AISC Specifications, Virginia Tech, 2001.
1.2D + 1.0L
1.2D + 1.0L
1.2D + 0.5Lr
2W
3W
4W
5W
6W
Nominal Loads
Gravity
Roof: D = 0.788 kip/ft
Lr = 1.890 kip/ft
Floor: D = 0.563 kip/ft
L = 3.378 kip/ft
Wind
W = 1.714 kip
Initial imperfection
Global sway D0 = H/500 (rightward)
Material
E = 29,000 ksi
Fy = 50 ksi
Load combination investigated
1.2D + 1.0L + 0.5Lr +1.0W

## Slide 14
Reference
Vogel, U. (1985), “Calibrating Frames”, Stahlbau, Vol. 10, pp 295-301.
6 @ 3.75m = 22.5m
2 @ 6.0m = 12.0m
Frame 12
HEB160
IPE400
HEB160
HEB220
HEB220
HEB220
HEB220
HEB200
HEB200
HEB240
HEB240
HEB260
HEB260
HEB160
HEB160
HEB220
HEB220
HEB220
HEB220
IPE400
IPE360
IPE360
IPE330
IPE330
IPE300
IPE300
IPE300
IPE300
IPE240
IPE240
W
1.2D + 1.0L
Nominal Loads
Gravity (L/D = 2)
Roof: D = 14.53 kN/m
Lr = 29.05 kN/m
Floor: D = 15.47 kN/m
L = 30.84 kN/m
Wind
Roof: W = 10.32 kN
Levels: W = 20.60 kN
Initial imperfection
Global sway D0 = H/500 (rightward)
Material
E = 205 kN/mm2
Fy = 235 N/mm2
Load combination investigated
1.2D + 1.0L + 0.5Lr +1.0W
W
W
W
W
W
1.2D + 1.0L
1.2D + 1.0L
1.2D + 1.0L
1.2D + 1.0L
1.2D + 0.5Lr

## Slide 15
Frame 13
10 @ 9’6”
3 @ 20’
Member Sizes |  |  |  | 
Level | Beams | Story | Exterior Columns | Interior Columns
Roof | W12x22 | 10 | W8x24 | W8x18
9 | W14x22 | 9 | W8x24 | W8x18
8 | W14x22 | 8 | W8x35 | W8x31
7 | W14x22 | 7 | W8x35 | W8x31
6 | W14x26 | 6 | W8x48 | W8x48
5 | W14x26 | 5 | W8x48 | W8x48
4 | W14x30 | 4 | W8x58 | W8x58
3 | W14x30 | 3 | W8x58 | W8x58
2 | W16x31 | 2 | W8x67 | W10x68
1 | W16x31 | 1 | W8x67 | W10x68
Reference
Lu, L.W., Ozer, E., Daniels, J.H., Okten, O.S., and Morino, S. (1975), “Frame Stability and Design of Columns in Unbraced Multistory Steel Frames”, Fritz Engineering Laboratory Report No. 375.2, Lehigh University, Bethlehem, Pennsylvania, July, 1975.
Nominal Loads
Gravity
Roof: D = 1.034 kip/ft
Lr = 0.778 kip/ft
Floor: D = 1.069 kip/ft
L = 0.778 kip/ft
Wall: D = 9.234 kip/story
Wind (rightward)
Roof: W = 3.189 kip
Levels: W = 6.379 kip
Initial imperfection
Global sway D0 = H/500 (rightward)
Material
E = 29,000 ksi
Fy = 36 ksi
Load combination investigated
1.2D + 1.0L + 0.5Lr + 1.0W

## Slide 16
3 @ 20’
2 @ 20’
2 @ 20’
Frame 14: Frame 13 with 4 lean-on columns
10 @ 9’6”
Reference
D.E. Statler, R.D. Ziemian, L.E. Robertson, The natural period as an indicator of second-order effects, Proceedings - Annual Stability Conference, Structural Stability Research Council. (2011) 136–147.
Nominal Loads
Gravity
Roof: D = 0.821 kip/ft
Lr = 0.616 kip/ft
Floor: D = 0.847 kip/ft
L = 0.616 kip/ft
Wall: D = 7.317 kip/story
Wind (rightward)
Roof: W = 2.835 kip
Levels: W = 5.669 kip
Initial imperfection
Global sway D0 = H/500 (rightward)
Material
E = 29,000 ksi
Fy = 36 ksi
Load combination investigated
1.2D + 1.0L + 0.5Lr + 1.0W

## Slide 17
3 @ 20’
2 @ 20’
2 @ 20’
Frame 15: Frame 13 with 8 lean-on columns
10 @ 9’6”
Reference
D.E. Statler, R.D. Ziemian, L.E. Robertson, The natural period as an indicator of second-order effects, Proceedings - Annual Stability Conference, Structural Stability Research Council. (2011) 136–147.
Nominal Loads
Gravity
Roof: D = 0.744 kip/ft
Lr = 0.558 kip/ft
Floor: D = 0.767 kip/ft
L = 0.558 kip/ft
Wall: D = 6.626 kip/story
Wind (rightward)
Roof: W = 2.290 kip
Levels: W = 4.579 kip
Initial imperfection
Global sway D0 = H/500 (rightward)
Material
E = 29,000 ksi
Fy = 36 ksi
Load combination investigated
1.2D + 1.0L + 0.5Lr + 1.0W

## Slide 18
3 @ 20’
2 @ 20’
2 @ 20’
Frame 16: Frame 13 with 12 lean-on columns
10 @ 9’6”
Reference
D.E. Statler, R.D. Ziemian, L.E. Robertson, The natural period as an indicator of second-order effects, Proceedings - Annual Stability Conference, Structural Stability Research Council. (2011) 136–147.
Nominal Loads
Gravity
Roof: D = 0.652 kip/ft
Lr = 0.489 kip/ft
Floor: D = 0.673 kip/ft
L = 0.489 kip/ft
Wall: D = 5.813 kip/story
Wind (rightward)
Roof: W = 2.006 kip
Levels: W = 4.012 kip
Initial imperfection
Global sway D0 = H/500 (rightward)
Material
E = 29,000 ksi
Fy = 36 ksi
Load combination investigated
1.2D + 1.0L + 0.5Lr + 1.0W

## Slide 19
Reference
Lu, L.W., Ozer, E., Daniels, J.H., Okten, O.S., and Morino, S. (1975), “Frame Stability and Design of Columns in Unbraced Multistory Steel Frames”, Fritz Engineering Laboratory Report No. 375.2, Lehigh University, Bethlehem, Pennsylvania, July, 1975.
Frame 17
10 @ 9’6”
5 @ 20’
Member Sizes |  |  |  | 
Level | Beams | Story | Exterior Columns | Interior Columns
Roof | W12x22 | 10 | W8x24 | W8x18
9 | W14x22 | 9 | W8x24 | W8x18
8 | W14x22 | 8 | W8x35 | W8x28
7 | W14x22 | 7 | W8x35 | W8x28
6 | W14x22 | 6 | W8x48 | W8x40
5 | W14x22 | 5 | W8x48 | W8x40
4 | W14x26 | 4 | W8x58 | W8x48
3 | W14x26 | 3 | W8x58 | W8x48
2 | W14x26 | 2 | W8x67 | W8x67
1 | W14x26 | 1 | W8x67 | W8x67
Nominal Loads
Gravity
Roof: D = 0.96 kip/ft
Lr = 0.72 kip/ft
Floor: D = 1.07 kip/ft
L = 0.78 kip/ft
Wall: D = 11.42 kip/story
Wind (rightward)
Roof: W = 2.969 kip
Levels: W = 5.938 kip
Initial imperfection
Global sway D0 = H/500 (rightward)
Material
E = 29,000 ksi
Fy = 36 ksi
Load combination investigated
1.2D + 1.0L + 0.5Lr + 1.0W

## Slide 20
Reference
Lu, L.W., Ozer, E., Daniels, J.H., Okten, O.S., and Morino, S. (1975), “Frame Stability and Design of Columns in Unbraced Multistory Steel Frames”, Fritz Engineering Laboratory Report No. 375.2, Lehigh University, Bethlehem, Pennsylvania, July, 1975.
Frame 18
1 @ 56’
20 @ 14’
Member Sizes |  |  | 
Level | Beams | Story | Columns
Roof | W30x99 | 19-20 | W14x132
15-19 | W33x130 | 17-18 | W14x176
13-14 | W36x135 | 15-16 | W14x233
11-12 | W36x150 | 13-14 | W14x257
9-10 | W36x160 | 11-12 | W14x311
8 | W36x170 | 9-10 | W14x370
6-7 | W36x182 | 7-8 | W14x426
3-5 | W36x194 | 5-6 | W14x500
1-2 | W36x230 | 3-4 | W14x550
 |  | 1-2 | W14x605
Nominal Loads
Gravity
Roof: D = 1.40 kip/ft
Lr = 1.06 kip/ft
Floor: D = 1.27 kip/ft
L = 1.90 kip/ft
Wall: D = 21.04 kip/story
Wind (rightward)
Roof: W = 6.39 kip
Levels: W = 12.78 kip
Initial imperfection
Global sway D0 = H/500 (rightward)
Material
E = 29,000 ksi
Fy = 36 ksi
Load combination investigated
1.2D + 1.0L + 0.5Lr + 1.0W

## Slide 21
Reference
Lu, L.W., Ozer, E., Daniels, J.H., Okten, O.S., and Morino, S. (1975), “Frame Stability and Design of Columns in Unbraced Multistory Steel Frames”, Fritz Engineering Laboratory Report No. 375.2, Lehigh University, Bethlehem, Pennsylvania, July, 1975.
Frame 19
26 @ 12’
3 @ 30’
Member Sizes |  |  |  | 
Level | Beams | Story | Exterior Columns | Interior Columns
Roof | W21x48 | 25-26 | W8x67 | W8x35
22-25 | W21x55 | 23-24 | W12x87 | W12x79
20-21 | W24x62 | 21-22 | W14x109 | W14x109
17-19 | W24x68 | 19-20 | W14x132 | W14x132
15-16 | W24x76 | 17-18 | W14x145 | W14x159
11-14 | W24x84 | 15-16 | W14x176 | W14x211
8-10 | W27x84 | 13-14 | W14x211 | W14x233
1-7 | W27x94 | 11-12 | W14x233 | W14x283
 |  | 9-10 | W14x257 | W14x311
 |  | 7-8 | W14x283 | W14x342
 |  | 5-6 | W14x311 | W14x370
 |  | 3-4 | W14x342 | W14x398
 |  | 1-2 | W14x370 | W14x426
Nominal Loads
Gravity
Roof: D = 1.40 kip/ft
Lr = 1.05 kip/ft
Floor: D = 1.26 kip/ft
L = 1.90 kip/ft
Wall: D = 21.04 kip/story
Wind (rightward)
Roof: W = 5.46 kip
Levels: W = 10.92 kip
Initial imperfection
Global sway D0 = H/500 (rightward)
Material
E = 29,000 ksi
Fy = 36 ksi
Load combination investigated
1.2D + 1.0L + 0.5Lr + 1.0W

## Slide 22
Reference
Lu, L.W., Ozer, E., Daniels, J.H., Okten, O.S., and Morino, S. (1975), “Frame Stability and Design of Columns in Unbraced Multistory Steel Frames”, Fritz Engineering Laboratory Report No. 375.2, Lehigh University, Bethlehem, Pennsylvania, July, 1975.
Frame 20
30 @ 12’
2 @ 30’
Member Sizes |  |  |  | 
Level | Beams | Story | Exterior Columns | Interior Columns
Roof | W24x55 | 29-30 | W14x74 | W14x43
24-29 | W24x76 | 27-28 | W14x109 | W14x82
22-23 | W24x84 | 25-26 | W14x145 | W14x132
20-21 | W27x84 | 23-24 | W14x176 | W14x159
17-19 | W30x90 | 21-22 | W14x211 | W14x211
14-16 | W30x99 | 19-20 | W14x257 | W14x257
11-14 | W30x108 | 17-18 | W14x283 | W14x311
8-10 | W30x116 | 15-16 | W14x342 | W14x342
1-7 | W33x118 | 13-14 | W14x370 | W14x398
 |  | 11-12 | W14x398 | W14x426
 |  | 9-10 | W14x455 | W14x455
 |  | 7-8 | W14x500 | W14x500
 |  | 5-6 | W14x550 | W14x550
 |  | 3-4 | W14x605 | W14x605
 |  | 1-2 | W14x605 | W14x730
Nominal Loads
Gravity
Roof: D = 1.60 kip/ft
Lr = 1.28 kip/ft
Floor: D = 1.77 kip/ft
L = 2.36 kip/ft
Wall: D = 25.58 kip/story
Wind (rightward)
Roof: W = 4.99 kip
Levels: W = 9.98 kip
Initial imperfection
Global sway D0 = H/500 (rightward)
Material
E = 29,000 ksi
Fy = 36 ksi
Load combination investigated
1.2D + 1.0L + 0.5Lr + 1.0W

## Slide 23
Reference
Lu, L.W., Ozer, E., Daniels, J.H., Okten, O.S., and Morino, S. (1975), “Frame Stability and Design of Columns in Unbraced Multistory Steel Frames”, Fritz Engineering Laboratory Report No. 375.2, Lehigh University, Bethlehem, Pennsylvania, July, 1975.
Frame 21
30 @ 12’
2 @ 30’
Member Sizes |  |  |  | 
Level | Beams | Story | Exterior Columns | Interior Columns
Roof | W21x44 | 29-30 | W10x60 | W10x39
27-29 | W21x57 | 27-28 | W14x82 | W14x68
26 | W24x62 | 25-26 | W14x99 | W14x99
24-25 | W24x68 | 23-24 | W14x132 | W14x145
21-23 | W24x76 | 21-22 | W14x145 | W14x176
19-20 | W24x84 | 19-20 | W14x176 | W14x211
17-18 | W27x84 | 17-18 | W14x211 | W14x233
14-16 | W27x94 | 15-16 | W14x257 | W14x283
10-13 | W30x99 | 13-14 | W14x283 | W14x311
7-9 | W30x108 | 11-12 | W14x311 | W14x342
1-6 | W30x116 | 9-10 | W14x342 | W14x370
 |  | 7-8 | W14x370 | W14x426
 |  | 5-6 | W14x398 | W14x455
 |  | 3-4 | W14x455 | W14x500
 |  | 1-2 | W14x500 | W14x550
Nominal Loads
Gravity
Roof: D = 1.28 kip/ft
Lr = 0.96 kip/ft
Floor: D = 1.15 kip/ft
L = 1.73 kip/ft
Wall: D = 19.13 kip/story
Wind (rightward)
Roof: W = 4.97 kip
Levels: W = 9.95 kip
Initial imperfection
Global sway D0 = H/500 (rightward)
Material
E = 29,000 ksi
Fy = 36 ksi
Load combination investigated
1.2D + 1.0L + 0.5Lr + 1.0W

## Slide 24
Reference
Lu, L.W., Ozer, E., Daniels, J.H., Okten, O.S., and Morino, S. (1975), “Frame Stability and Design of Columns in Unbraced Multistory Steel Frames”, Fritz Engineering Laboratory Report No. 375.2, Lehigh University, Bethlehem, Pennsylvania, July, 1975.
Frame 22
2 @ 30’
40 @ 12’
Member Sizes |  |  |  | 
Level | Beams | Story | Exterior Columns | Interior Columns
Roof | W21x44 | 39-40 | W10x60 | W10x39
38-39 | W21x55 | 37-38 | W12x87 | W12x72
36-37 | W24x62 | 35-36 | W14x109 | W14x109
34-35 | W24x68 | 33-34 | W14x132 | W14x132
32-33 | W24x76 | 31-32 | W14x145 | W14x176
29-31 | W24x84 | 29-30 | W14x176 | W14x211
26-28 | W27x94 | 27-28 | W14x211 | W14x233
22-25 | W30x99 | 25-26 | W14x257 | W14x283
19-21 | W30x108 | 23-24 | W14x283 | W14x311
15-18 | W30x116 | 21-22 | W14x311 | W14x342
11-14 | W33x118 | 19-20 | W14x370 | W14x370
1-10 | W33x130 | 17-18 | W14x398 | W14x398
 |  | 15-16 | W14x426 | W14x426
 |  | 13-14 | W14x455 | W14x455
 |  | 11-12 | W14x500 | W14x500
 |  | 7-10 | W14x550 | W14x550
 |  | 5-6 | W14x605 | W14x605
 |  | 3-4 | W14x665 | W14x665
 |  | 1-2 | W14x730 | W14x730
Nominal Loads
Gravity
Roof: D = 1.22 kip/ft
Lr = 0.91 kip/ft
Floor: D = 1.10 kip/ft
L = 1.65 kip/ft
Wall: D = 18.23 kip/story
Wind (rightward)
Roof: W = 4.74 kip
Levels: W = 9.48 kip
Initial imperfection
Global sway D0 = H/500 (rightward)
Material
E = 29,000 ksi
Fy = 36 ksi
Load combination investigated
1.2D + 1.0L + 0.5Lr + 1.0W